## Slide 1: Branch Prediction
What is the optimal choice of branch prediction method?
Alison Davis
CIS655 – 3/3/2020

## Slide 2: Motivation
Increasing ILP
Goal: minimizing stall cycles
Optimization problem
  Accuracy
  Complexity/Code Size
  Energy

## Slide 3: Existing Methods
Dynamic Prediction Methods
Local vs Global
BHT (Branch History Table)
Aliasing
Static Prediction Methods
Profiling & tracing
Heuristics & Bias
Additional Considerations
Combinational Methods

## Slide 4: The best method of branch prediction…?
…it depends.
But, if I had to have an opinion..

## Slide 5: SimpleScalar Demo

## Slide 6: BP Method Accuracies in SimpleScalar
Chart: Accuracies for different bp methods in simplescalar
| taken | bimod | comb | 2lev
 | 0.3352 | 0.9108 | 0.9199 | 0.8455

## Slide 7: Increasing History Bits: Accuracy & Cache Miss Rate
Iterations of 2lev in SimpleScalar
  M <l1size>
  N <l2size>
  W <hist_size>
  X <Xor>
SimpleScalar Default: M, N, W, X = 1,1024, 8, 0
GAg = Global History Reg & Global Pattern History Table

## Slide 8: Data for Varying History Width
Type of Predictor | M | N | W | X | Accuracy | Level 1 Cache Miss Rate
2lev | <1> | <2^W> | <W> | <0> |  | 
 | 1 | 2 | 1 | 0 | 0.6438 | 0.0607
 | 1 | 4 | 2 | 0 | 0.6507 | 0.0616
 | 1 | 16 | 4 | 0 | 0.6726 | 0.062
 | 1 | 256 | 8 | 0 | 0.7466 | 0.0625
 | 1 | 1024 | 10 | 0 | 0.7849 | 0.063
 | 1 | 32768 | 15 | 0 | 0.8049 | 0.0629
 | 1 | 1048576 | 20 | 0 | 0.8029 | 0.0624

## Slide 9: Branch Prediction Accuracy for Increasing History Size in GAg Method
Chart: Accuracy Rate vs History Width for GAg BP Method
| 1 | 2 | 4 | 8 | 10 | 15 | 20
 | 0.6438 | 0.6507 | 0.6726 | 0.7466 | 0.7849 | 0.8049 | 0.8029
GAg = Global History Reg & Global Pattern History Table

## Slide 10: L1 Instruction Cache Miss Rate for Increasing History Size in GAg Method
Chart: L1 Instruction Cache Miss Rate vs History Width for GAg BP Method
| 1 | 2 | 4 | 8 | 10 | 15 | 20
 | 0.0607 | 0.0616 | 0.062 | 0.0625 | 0.063 | 0.0629 | 0.0624
GAg = Global History Reg & Global Pattern History Table